TIK-4
Komunikasi Data : Mode Transmisi, Modulasi,	Hardware
@btatmaja

---
Transmisi Digital
- Data ditransmisikan dalam bentuk sinyal
- Untuk mengirim data secara digital, sinyal harus dikonversi dalam bentuk digital
  - Digital to Digital Conversion
  - Analog to Digital Conversion
- Mode Transmisi
  - Synchronus Transmission
  - Asynchronus Transmission

---
Digital to Digital Conversion
Proses konversi digital to digital → Line Coding

---
ADC: Sampling

---
ADC: Quantization

---
ADC: Encoding

---
Mode Transmisi: Parallel

---
Mode Transmisi: Serial
Mode transmisi serial bisa berupa salah satu asynchronus atau synchronus

---
Asynchronus Vs Synchronus
Asynchronus	Synchronus
No impportance of Timing	Timing is controlled
During idle condition Signal ‘1’ is transmitted	No idle, clock is used to sync
“Start bit” before the byte and “Stop bit” at the end of the byte for Start/Stop synchronisation → more bit	No Start/Stop bits → less bit
Satu kesalahan → merusak satu karakter	Satu kesalahan merusak satu blok

---
Modulasi
- Dalam komunikasi, hanya range frekuensi tertentu saja yang bisa ditransmisikan
- Untuk mengirim data yang tidak dalam cakupan range frekuensi tersebut, maka data perlu “ditumpangkan” pada range frekuensi yang dijinkan
- Teknik penumpangan suatu frekuesi (fs) pada frekuensi pembawa (fc) tersebut dinamakan modulasi

---
Modulasi: Analog
- Modulasi:
  - Analog
  - Digital
- Modulasi Analog
  - Amplitude Modulation (AM)
  - Frequency Modulation (FM)
  - Phase Modulatio (PM)

---
Amplitude Modulation

---
FM dan PM

---
Digital Modulation

---
Digital Modulation

---
Analog Transmission
  - Digital to analog conversion : data is converted into bandpass analog signals
  - When data is sent via analog carrier, it is converted into analog signal
  - Analog signal is modified to reflect binary data
  - Analog signal is characterized by its amplitude, frequency, phase.
  - Analog-to-analog conversion: ASK, FSK dan PSK

---
Amplitude Shift Keying
 amplitude of analog carrier signal is modified to reflect binary data.

---
FSK
the frequency of the analog carrier signal is modified to reflect binary data.

---
Phase Shift Keying
the frequency of the analog carrier signal is modified to reflect binary data.

---
Modem
- MoDem = Modulator – Demodulator
- Internal modem, plugin/on board komputer dapat dihubungkan langsung dengan telefon
- Eksternal, berada di luar komputer dan dihubungkan dengan komputer melalui port serial (USB).