TIK-6
Komunikasi Data: Modulasi, Mux, CDMA, PSTN, ADSL
@btatmaja

---
Overview
- Modulasi
- Multiplexing
- CDMA
- PSTN
- ADSL

---
Modulasi

---
Frequency Division Multiplexing (FDM)
- FDM (Frequency Division Multiplexing) takes advantage of passband transmission to share a channel. It divides the spectrum into frequency bands, with each user having exclusive possession of some band in which to send their signal.
- AM radio broadcasting illustrates FDM. The allocated spectrum is about 1 Mhz, roughly 500 to 1500 kHz. Different frequencies are allocated to different logical channels (stations), each operating in a portion of the spectrum

---
FDM

---
Orthogonal FDM (FDM)

---
Time Domain Multiplexing
- each one periodically getting the entire bandwidth for a little burst of time
- Bits from each input stream are taken in a fixed time slot and output to the aggregate stream

---
Code Division Multiple Access (CDMA)
- Spread spectrum communication in which a narrowband signal is spread out over a wider frequency band
- CDMA allows each station to transmit over the entire frequency spectrum all the time
- the key to CDMA is to be able to extract the desired signal while rejecting everything else as random noise

---
PSTN
- PSTN --> Public Switched Telephone Network
- Transmitting the human voice in a more-or-less recognizable form

---
ADSL
DSL --> Digital Subscriber Line, type of Modem with high speed

---
ADSL
- ADSL adalah pentransferan date berkecapatan tinggi dengan menggunakan saluran telepon (DSL)
- Layanan ASL misal VOD (Video on Demand): TV, Movie, dsb
- Kecepatan ADSL: 1.5 Mbps s/d 13 Mbps

---
ADSL

---
ADSL Conf